## Slide 1: CacheBandit
A Framework Towards Improving Shared Tightly-Coupled-Memory ($) Efficiency in Embedded SIMT Architectures.

## Slide 2: Introduction
Multiple contemporary Scientific Computing / Industrial (HPC) applications involve Sparse-Matrix (SpM) solvers, such as in FEM, CFD, Structural-Modeling, Graph Processing, and AI Edge-Inference [1 - 5].
SpM streaming kernels such as SpMV are memory-bound rather than compute-bound. Largely limited by the available bandwidth between compute units and off-chip memory, through the memory hierarchy.

## Slide 3: Introduction
Multiple contemporary Scientific Computing / Industrial (HPC) applications involve Sparse-Matrix (SpM) solvers [1 - 5].
SpM streaming kernels tend to be memory-bound rather than compute-bound [6].
Hence benefiting from Near-Data-Processing (NDP) architectures.

## Slide 4: Introduction: Memory Bottleneck Classes
* [6]

## Slide 5: Introduction: Near Data Processing (NDP)
* [6]

## Slide 6: Case Study: SpMV
SpMV is ubiquitous in HPC and is chosen for NDP cache enhancement study due to high LFMR and high MPKI.
SpMV kernels are currently run on GPGPUs [8, 9] with compute-centric architectures.
SIMT architecture maximum throughput achieved by scheduling workloads across threads to hide latencies [10].
SpMV streams on SIMT exhibit poor temporal locality. Resulting in exacerbated cache line (thrashing) conflicts [11].

## Slide 7: SpMV: Representation
* [12]

## Slide 8: Problem: Cache Resource Contention
Thrashing of a ‘Set-Associative’ (SA) TCM$ (L1D) due to multiple physical addresses mapping to the same block/line/frame.
  -> Barrier = Hardware implementing Associativity (Field-of-View).
Results in increased DRAM memory traffic due unnecessary evictions in TCM$.
  -> Barrier = Cache contention (SA mapping).
Thus, requiring larger DRAM bandwidth, leading to:
  (1) Slower execution time -> Tspmv_lower_bound ∝ No. of DRAM access.
  (2) Higher energy consumption -> Espmv_lower_bound ∝ No. of DRAM access.
  (3) Lower Cache Efficiency -> Bloating of DRAM access beyond necessary.

## Slide 9: Problem:
*https://gpuopen.com/learn/amd-lab-notes/amd-lab-notes-spmv-docs-spmv_part1/

## Slide 10: Problem:
* [11]

## Slide 11: Problem:
* [11]

## Slide 12: Problem
* [11]

## Slide 13: Problem: Embedded Platform
SpMV on deep-cache-hierarchy architectures (GPGPU/CPU) can suffer from additional latency introduced by the hierarchy, due to their low arithmetic intensity.
Hence the FPGAs prototype-ability is used to study the effect of NDP cache enhancements on embedded SpMV accelerators.
High-Level-Synthesis (HLS) reduces the effort to port C/C++ SpMV algorithms to FPGA accelerators [12].

## Slide 14: Problem:
* [10]

## Slide 15: Problem:
* [6]

## Slide 16: Solution Space Exploration:
Many approaches exist to reduce cache conflict. Some [13 - 15] involve cache/thread/load-aware scheduling and pre-processing techniques (Access-Pattern-Manipulation) to improve L1D$ utilization.
Other approaches [16 - 20] involve hardware enhancements (Access-Pattern Adaptation) to remedy cache resource conflicts.
In practice, effort on both APM and APA fronts are necessary to maximize $ utilization in irregular memory access patterns.
This work (CacheBandit) falls under the second category of APM enhancement, for NDP SIMT architectures.

## Slide 17: CacheBandit: Goals
Major goals:
  (1) Reduce cache contention (FA + larger FOV) and maximize TCM$ efficiency.
  (2) Support concurrent (TDM) Multi-Context access.
  (3) Tile-able (structurally) / Scalable (Frequency) (Little’s Law).
Target TCM/L1D$ which is present in both compute/memory centric architectures.

## Slide 18: CacheBandit: Hypothesis
If cache contention (FOV) is the bottleneck and not the cache size, as in the case with streaming applications such as SpMV.
Solution is to use ‘Fully-Associative’ (FA) cache.
But realizing FA cache resources across threads sharing TCM$ is expensive.
Hence, employ a hybrid solution. The TCM$ is FA from a physical memory perspective, but is virtually SA with respect to each individual thread.

## Slide 19: CacheBandit:

## Slide 20: CacheBandit: Flow

## Slide 21: CacheBandit: Single Warp Simulation

## Slide 22: CacheBandit:

## Slide 23: CacheBandit:

## Slide 24: CacheBandit: Performance Metrics
Chart: 
| bcsstk10 | bcsstk13 | bcsstk17 | c8_mat11 | cq9 | fv1 | kl02 | lhr34c | pdb1HYS | psmigr_1 | wiki-Vote | p2p-Gnutella04 | ca-HepTh | as-735 | amazon0312 | KM_2000 | KM_3000 | KM_4000 | KM_5000
DRAM Access Reduction | 0 | 9.3525 | -10.9329 | 17.1491 | 11.1594 | 0 | 0.56096 | -0.074294 | -11.4834 | 12.1519 | -2.7223 | -2.4533 | -0.11145 | -8.5128 | -0.27767 | 0 | 35.7624 | 16.4941 | 9.1822

## Slide 25: CacheBandit:
Chart: Cache Hit-Rate
| bcsstk10 | bcsstk13 | bcsstk17 | c8_mat11 | cq9 | fv1 | kl02 | lhr34c | pdb1HYS | psmigr_1 | wiki-Vote | p2p-Gnutella04 | ca-HepTh | as-735 | amazon0312 | KM_2000 | KM_3000 | KM_4000 | KM_5000
Baseline Hit-Rate | 99.6919 | 99.8343 | 99.84 | 93.2343 | 60.9955 | 99.2951 | 82.6378 | 99.6477 | 99.8585 | 84.2601 | 59.0824 | 51.2827 | 25.7624 | 69.6414 | 52.49 | 99.9969 | 93.7333 | 93.75 | 93.74
CacheBandit Hit-Rate | 99.6919 | 99.8498 | 99.8225 | 94.3945 | 65.3482 | 99.2951 | 82.7352 | 99.6474 | 99.8422 | 86.1728 | 57.9685 | 50.0875 | 25.6797 | 67.0571 | 52.3581 | 99.9969 | 95.9744 | 94.7809 | 94.3148

## Slide 26: CacheBandit:
Problem: Name = cq9, Group = Meszaros, Kind = linear programming problem.
K = 9278, M = 21534 ; Density = 4.83% ; NNZ = 96653 ; Unique Frames Visited = 1346

## Slide 27: CacheBandit: Dynamic Virtual Sets
Chart: 
| bcsstk10 | bcsstk13 | bcsstk17 | c8_mat11 | cq9 | fv1 | kl02 | lhr34c | pdb1HYS | psmigr_1 | wiki-Vote | p2p-Gnutella04 | ca-HepTh | as-735 | amazon0312 | KM_2000 | KM_3000 | KM_4000 | KM_5000
DRAM Access Reduction | 0 | 9.3525 | 0 | 18.0487 | 10.4114 | 0 | 0.64226 | 0 | 0 | 12.1647 | 0 | 0 | 0 | 0 | 0 | 0 | 35.8837 | 16.5495 | 9.1822

## Slide 28: CacheBandit:
Chart: Cache Hit-Rate
| bcsstk10 | bcsstk13 | bcsstk17 | c8_mat11 | cq9 | fv1 | kl02 | lhr34c | pdb1HYS | psmigr_1 | wiki-Vote | p2p-Gnutella04 | ca-HepTh | as-735 | amazon0312 | KM_2000 | KM_3000 | KM_4000 | KM_5000
Baseline Hit-Rate | 99.6919 | 99.8343 | 99.84 | 93.2343 | 60.9955 | 99.2951 | 82.6378 | 99.6477 | 99.8585 | 84.2601 | 59.0824 | 51.2827 | 25.7624 | 69.6414 | 52.49 | 99.9969 | 93.7333 | 93.75 | 93.74
CacheBandit Hit-Rate | 99.6919 | 99.8498 | 99.84 | 94.4554 | 65.0564 | 99.2951 | 82.7493 | 99.6477 | 99.8585 | 86.1748 | 59.0824 | 51.2827 | 25.7624 | 69.6414 | 52.49 | 99.9969 | 95.982 | 94.7843 | 94.3148

## Slide 29: CacheBandit: Multi Warp Simulation

## Slide 30: CacheBandit: Multi Warp

## Slide 31: CacheBandit: Multi Warp Metrics
Chart: 
| bcsstk10 | bcsstk13 | bcsstk17 | c8_mat11 | cq9 | fv1 | kl02 | lhr34c | pdb1HYS | psmigr_1 | wiki-Vote | p2p-Gnutella04 | ca-HepTh | as-735 | amazon0312
DRAM Access Reduction | 0 | 0 | -29.3003 | 97.2112 | 55.2978 | 0 | 1.6418 | 4.2667 | 16.7292 | 77.7652 | 94.3445 | 53.9286 | 44.8996 | 85.7441 | -0.50284

## Slide 32: CacheBandit: Multi Warp
Chart: Cache Hit-Rate
| bcsstk10 | bcsstk13 | bcsstk17 | c8_mat11 | cq9 | fv1 | kl02 | lhr34c | pdb1HYS | psmigr_1 | wiki-Vote | p2p-Gnutella04 | ca-HepTh | as-735 | amazon0312
Baseline Hit-Rate | 99.8046 | 99.9048 | 99.8971 | 99.2499 | 85.6346 | 99.5195 | 85.4524 | 99.7159 | 99.9022 | 99.8824 | 90.1635 | 84.0156 | 71.3546 | 87.5353 | 46.0782
CacheBandit Hit-Rate | 99.8046 | 99.906 | 99.8707 | 99.9851 | 94.5224 | 99.5211 | 87.2609 | 99.7887 | 99.9338 | 99.975 | 99.5143 | 93.1356 | 84.434 | 98.3839 | 49.2518

## Slide 33: CacheBandit: Single Warp Template

## Slide 34: CacheBandit: Implementation Roadmap
Parts:
  (1) Allocator: Provide solution to thread upon cache line request.
  (2) Virtual L1: Tag store, comparator hardware.
  (2) Deallocator: Reclaim cache lines upon hitting utilization threshold.
  (4) Memory Controller: DMA with DRAM memory.
Sub-modules allocator and deallocator are ported from QuickPage(Lite).
MCU and Virtual L1 tag array still need to be worked out.

## Slide 35: CacheBandit: Advantages
Eliminates conflict-miss within a SIMT core.
Template design reduces design overhead.
Scalable in terms of both:
  Managed Cache capacity.
  Core frequency.

## Slide 36: CacheBandit: Tradeoffs
Implementation cost grows with core frequency and managed page size (solution space).
Still very dependent on memory access pattern.
Not a standalone solution, and requires pre-processing such as access pattern profiling to set dynamic sets.

## Slide 37: CacheBandit: QPL Resource Dependency
Chart: Single-Port LUT Utilization
| 16 | 32 | 64 | 128 | 256 | 512
SP2 | 1 | 2 | 3 | 6 | 13 | 30
SP4 | 1 | 2 | 4 | 8 | 17 | 39
SP8 | 2 | 3 | 5 | 12 | 25 | 56
SP16 | 2 | 5 | 9 | 20 | 41 | 91

## Slide 38: Bibliography
[1] Efficient Computation of Sparse Matrix Functions for Large-Scale Electronic Structure Calculations: The CheSS Library, Stephan Mohr, et.al.
[2] Multi-level μ-Finite Element Analysis for Human Bone Structures, Peter Arbenz, et.al.
[3] Sparse Matrix Algebra for Quantum Modeling of Large Systems, Emanuel H. Rubensson, et.al.
[4] SparseGPT: Massive Language Models Can be Accurately Pruned in One-Shot, Elias Frantar, Dan Alistarh.
[5] Sparse Linear Algebra Toolkit for Computational Aerodynamics, Stephen L. Wood, et.al.
[6] DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks, Geraldo F. Oliveira, et.al.
[8] NVIDIA AMPERE GA102 GPU ARCHITECTURE (white paper)
[9] CUDA Programming A Developer’s Guide to Parallel Computing with GPUs, Shane Cook (book)
[10] Understanding Latency Hiding on GPUs, Vasily Volkov (PhD)
[11] Reducing Cache Contention On GPUs, Kyoshin Choo (PhD)
[12] Optimization of sparse matrix–vector multiplication on emerging multicore platforms, Samuel Williams, et.al.
[13] A Streaming Dataflow Engine for Sparse Matrix-Vector Multiplication using High-Level Synthesis, Mohammad Hosseinabady, and Jose Luis Nunez-Yanez
[14] Efficient Algorithm Design of Optimizing SpMV on GPU, Genshen Chu, et.al.
[15] Locality-Aware CTA Clustering for Modern GPUs, Ang Li, et.al. (includes Prof. Akash Kumar)
[16] OWL: Cooperative Thread Array Aware Scheduling Techniques for Improving GPGPU Performance, Adwait Jog, et.al. (includes Prof. Onur Mutlu)
[17] Locality-Based Cache Management and Warp Scheduling for Reducing Cache Contention in GPU, Juan Fang, et.al.
[18] Warp Scheduling for Fine-Grained Synchronization, Ahmed ElTantawy, Tor M. Aamodt
[19] An Efficient GPU Cache Architecture for Applications with Irregular Memory Access Patterns, Bingchao Li, et.al.
[20] ATA-Cache: Contention Mitigation for GPU Shared L1 Cache with Aggregated Tag Array, Xiangrong Xu, et.al.
[21] Dynamically linked MSHRs for adaptive miss handling in GPUs, Yongbin Gu, Lizhong Chen

## Slide 39: Thank You!